## Slide 1: CHEMISTRY 1105
Exploring Boyle’s Law using Vernier Equipment

## Slide 2: Pressure vs. Volume
VERNIER EQUIPMENT OVERVIEW:
CHEMISTRY 1105
Lab Quest 2
Syringe
Gas Pressure
Sensor
Power Connection
Stylus
Gas Pressure Sensor connected
to Analog Port at
side of Lab Quest 2

## Slide 3: Pressure vs. Volume
CONNECTIONS & POWER:
CHEMISTRY 1105
Power Connection
Power Button

## Slide 4: Pressure vs. Volume
Tap on the number shown in the red Pressure box to change the units from the default kPa to atm.
CHEMISTRY 1105

## Slide 5: Pressure vs. Volume
Tap on the Mode box to change the setting to Events with Entry.
Name the Event Volume and enter the units as mL.
CHEMISTRY 1105

## Slide 6: Pressure vs. Volume
10.5mL
Syringe is attached to the pressure sensor with a volume of 10.0mL of AIR.
CHEMISTRY 1105

## Slide 7: Pressure vs. Volume
Tap on the Gauge Icon . Push the plunger to 5.0 mL and see that the pressure is stable.
Warning do NOT let the pressure go above 2.0 atm, it will damage the sensor.
Hold the plunger on the syringe throughout the experiment
CHEMISTRY 1105

## Slide 8: Pressure vs. Volume
Adjust the Syringe to 5.0 mL and press the Start Button on the Lab Quest 2.
Increase the volume in 1 mL stages until you reach 20.0mL. Maintain a steady volume when you are ready and record volume values by pressing the Keep Icon.
CHEMISTRY 1105
8.0mL
10.5mL
13.5mL
20.0mL
20.0mL

## Slide 9: Pressure vs. Volume
You should have at least 12 different data points after completing the experiment.
Press the Stop Button to stop collecting data.
Tap on the X/Y Table Icon . Record the data shown in the Run table into your lab notebook.
Click on Graph Icon to view the data points on a grid. Make a rough sketch in your notebook of the graph.
CHEMISTRY 1105

## Slide 10: Pressure vs. Volume
Shut down the Lab Quest 2.
Turn the Power Off by pressing the Power button.
Graph your data using Excel.
Graph Pressure (atm) versus Volume (mL) and Pressure (atm) versus 1/Volume (mL-1). Which graph gives a linear relationship?
Create a graph in Excel. Go to http://kwantlen.ca/science/chemistry/chem1210/richsup/excel.pdf
CHEMISTRY 1105